## Slide 1: FTC: Introduction to CAD/CAM
Team 13380 Quantum Stingers

## Slide 2: Intro
CAD/CAM stands for Computer Aided Design/Computer Aided Manufacturing
Can be helpful to sketch or design to 3D print or cut via CNC
By designing a 3d model, you can assure that parts fit in their intended assembly before buying them
Can help create computerized/digital assemblies or models for ease of design along the design process
For assemblies of robot, you can find bought parts from their respective online vendors (Pitsco, GoBilda, etc.) and import into your model
Going forwards, becoming more advanced, it can be used to simulate real life conditions, testing certain builds without actually needing to build them
There are many CAD softwares out there, but the main ones used for FTC are Fusion 360, Inventor, and Solidworks

## Slide 3: Fusion 360 Recommended RAM: 4 GB
Pros:
  Cloud-based
  Runs directly on both Windows and Mac OS
  Allows for team collaboration on shared projects
  Has simulation features
  3 year free educational license
  Lots of material available so easier to pick up/learn for beginners
Cons:
  If you have bad internet, will frequently be slow
  Can’t handle as complex builds as effectively as Inventor

## Slide 4: Inventor Recommended RAM: 20 GB
Pros:
  Runs directly on Windows
  More powerful/complex than Fusion 360, so can handle more complicated/intricate designs
  1 year free educational license
Cons:
  Since it stores files on your hard drive, exporting files will not be as smooth/automated as cloud-based softwares like Fusion 360
  Thus, harder for collaboration of whole team
  More powerful/complex than Fusion 360, so can be a bit overwhelming at first for beginners to learn
  Doesn’t run directly on Mac OS

## Slide 5: Solidworks Recommended RAM: 16 GB
Pros:
  Can be local or cloud-based
  Runs directly on Windows
  Can handle very large/complicated designs and assemblies
  Can export directly to AR/VR applications for even more immersed interactions with CAD models
  Best simulation tools/features out of all the three
Cons:
  Doesn’t run directly on Mac OS
  No free educational license, instead only perpetual or subscription license

## Slide 6: Basic CAD Tutorial
Most CAD systems are very similar, so here is our tutorial based on Fusion 360; No matter which system you decide on this tutorial will help
Here’s how to get started/how we got started:
Step 1: Get an Autodesk account
Go to https://www.autodesk.com/products/fusion-360/students-teachers-educators
Click Create Account (steps to creating should be self explanatory) and verify via email
Step 2: Get access to the software
Go back to https://www.autodesk.com/products/fusion-360/students-teachers-educators
Click Get Access, then Download and run the .exe setup file

## Slide 7: Creating Your First File
Step 3: Create your first project!
After launching up Fusion 360 for the first time, you should see a blank workspace and a dashboard area to the left
Click New Project and name it

## Slide 8: Learning to Use
Step 4: Learn to use
Double click the project you just made to enter it
You should see a blank project page in your dashboard area
Now, you can upload files through the blue upload button
In addition, anything you start making in the workspace can now be saved to your project

## Slide 9: Uploading Files
Step 4: Learn to upload
Google up your desired component, and go to its product page
Find an area for “Resources” or “Downloads” something of the like, in which you can download the component as a .step file

## Slide 10: Uploading Files
Step 4 cont.: Learn to upload
Go to back to Fusion and click Upload. You can select what you just downloaded (may need to be unzipped) & upload it (may take a while)
When done/completed, the file should appear in the dashboard area, now no longer blank
Save the Untitled design to keep/edit it (In the future, version description when saving is good to fill out specifically to what iteration you made this session to keep track but is not necessary). Now it is in you project page dashboard area.
Right click your component and click “Insert into Current Design”, or simply click and drag it into the left (now blank) workspace
Tada! You now have your first assembly!

## Slide 11: More CAD Tutorials
That was just a brief basic tutorial to get used to the file structure of Fusion 360
Uploading is great if you have existing parts or files from other sources
  Will be used a lot in assembly, in which you put parts together to pseudo-build it and make a model there on CAD
Other tutorials for other skills in CAD (sketching, animating, etc.) can be found online
  Some personally recommended courses are:
    Autodesk’s own tutorials for Fusion 360
      https://f360ap.autodesk.com/courses
        https://f360ap.autodesk.com/courses/getting-started-in-fusion-360/lessons/course-overview -for beginners/to start off
    Autodesk’s own tutorials for Inventor
      https://academy.autodesk.com/software/inventor-tutorial
    SolidWorks lessons
      http://solidworkstutorialsforbeginners.com/solidworks-tutorials-for-beginners/
      http://www.solidworkstutorials.com/

## Slide 12: Credits
This lesson was written by Alvin Lin for FTCTutorials.com
You can contact the author Alvin Lin at alvinlinsv@gmail.com
ADD YOUR TEAM LOGO HERE
More lessons for FIRST Tech Challenge are available at www.FTCtutorials.com
This work is licensed under a
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.